## Slide 1: Update Helmet Noninvasive Ventilation J. Gotchall, MD Mar. 31, 2020
This is keeping it short, giving you resources
Helmet Noninvasive Ventilation, Italian model
  Don’t think of HNIV as BiPAP/CPAP
  Do think of HNIV as Big Mixing Chamber with
    High Flow Oxygen (FiO2 ~ 73%) and
    PEEP 5-20 cm and
    Expiratory Limb Filter.
  Less particle droplet dispersion than HFNC or facemask interface

## Slide 2: How to do this linked here
Screenshot of 8-bed HNIV ICU in Italy, Today Show, March 21, 2020

## Slide 3: Materials List
DEVICE | Components | Description | Resource | Cost, estimate | Comment
Sea-Long Helmet | Sea-Long Helmet | Helmet Oxygen Tent | at www.Sea-Long.com |  | Tested, backorder
Amron Helmet | Amron Helmet | Helmet Oxygen Tent | at www.amronintle.com |  | 
 | Wall Gas Source, High Flow |  |  |  | 
 | Inspiratory Limb | (3) Gas Regulators | (2) Oxygen (flush) | (1) Medical Gas (flush) | 
 |  | (3) Oxygen Tubing (7-foot) |  | $1 / ea | 
 |  | (1) length standard corragated tubing |  | $0.18 / ft | 
 |  | (1) Concha Tube Adapter | Hudson RCI 384-00 | $2 / ea | 
 |  | (2) Oxygen enrichment attachment | Respirionics 312710 | $5-7 / ea | 
 |  | (1) 15 mm I.D./22 mm O.D. adapter |  | $0.44 / ea | 
 |  | Humidity (optional, intermittent) |  |  | 
Just a sample, more complete list on my Google Drive folder linked here

## Slide 4: Supply Chain Issues
“Just in time inventory” makes little sense for resp or PPE today
  Orders drive production
  Expedite w/ Prepaid Orders
  Remember: DME/Resp equipment is “durable” Resp equipment generally nonperishables with long shelf life
  Maybe hospitals/states can redistribute surplus to areas of need
  Anticipate shortages in
    Ventilators
    Helmets
    PEEP valves
    Other oxygen circuit supplies

## Slide 5: Reminders
Happy to discuss
Google Drive Folder with details linked here
  Work in progress
  Expect iterations
Send us your results and experiences! OFRRmail@gmail.com
Fill out the survey
Conflicts of Interest: none